## Slide 1
COMPUTER NETWORKS PROJECT
Small Office Network using VLANs, Inter-VLAN Routing and DHCP
Cisco Packet Tracer | Secure, segmented office network
TEAM MEMBERS
Ravindra Swami
Jash Chordiya
Pratyush Kumar Sahoo
Departmental segmentation • Automated addressing • Access control
SMALL OFFICE NETWORK | CISCO PACKET TRACER
1

## Slide 2
Problem Statement & Motivation
01 • PROBLEM
The problem
• A flat office network puts all departments in one broadcast domain.
• Manual IP configuration takes time and can cause addressing errors.
• Unrestricted communication can expose confidential departmental devices.
• Troubleshooting becomes harder as the office network grows.
Why it matters
SEGMENTATION
Separate HR, IT and Sales into logical VLANs.
AUTOMATION
Use DHCP to assign client addresses automatically.
CONTROLLED ACCESS
Use an ACL to restrict Sales access to HR devices.
SMALL OFFICE NETWORK | CISCO PACKET TRACER
2

## Slide 3
Existing Approach (Baseline) & Its Gaps
02 • BASELINE
FLAT NETWORK BASELINE
• One shared network • Broad broadcast domain • Manual IP setup possible • Little separation between departments
GAPS
• Unnecessary inter-department visibility • Addressing errors from manual setup • No central name-based access • Security policies harder to enforce
PROPOSED APPROACH
• VLAN 10: HR • VLAN 20: IT • VLAN 30: Sales • Router-on-a-Stick + DHCP + ACL
Baseline is a conceptual comparison unless a separate flat-network simulation was built and measured.
SMALL OFFICE NETWORK | CISCO PACKET TRACER
3

## Slide 4
Proposed Solution & Novelty
03 • PROPOSED
What this project brings together
VLAN segmentation
Separate HR, IT and Sales broadcast domains.
Router-on-a-Stick
Route between VLANs using one router physical interface and 802.1Q trunk.
DHCP automation
Assign IP settings dynamically to client PCs.
Server services
Provide internal DNS name resolution and HTTP company portal.
Layer 2 + Layer 3 security
Sticky MAC port security and extended ACL rules.
SMALL OFFICE NETWORK | CISCO PACKET TRACER
4

## Slide 5
Network Architecture
04 • ARCHITECTURE
R1 • Cisco 2911
Gateways • DHCP • ACL
SW1 • Catalyst 2960
VLANs • Trunk • Port Security
802.1Q trunk
HR • VLAN 10
3 PCs • 192.168.10.0/24
IT • VLAN 20
3 PCs • 192.168.20.0/24
SALES • VLAN 30
3 PCs • 192.168.30.0/24
Company Server
192.168.10.10 • DNS + HTTP
Note: Server is connected to SW1 access port Fa0/10 in VLAN 10.
SMALL OFFICE NETWORK | CISCO PACKET TRACER
5

## Slide 6
Implementation Setup
05 • SETUP
HARDWARE / DEVICES
• 1 × Cisco 2911 router • 1 × Catalyst 2960 switch • 9 × PCs (3 per department) • 1 × Server-PT • Copper Ethernet links
ADDRESSING
• HR: 192.168.10.0/24 • IT: 192.168.20.0/24 • Sales: 192.168.30.0/24 • Gateway: .1 in each subnet • DHCP clients: .21 onward • Server: 192.168.10.10 static
CONFIGURATION
• VLANs 10, 20, 30 • 802.1Q trunk on SW1 Gi0/1 • Router subinterfaces Gi0/0.10/.20/.30 • DHCP pools and exclusions • DNS record: company.local • HTTP service enabled
Tool: Cisco Packet Tracer. Device support and configuration are verified in the saved simulation.
SMALL OFFICE NETWORK | CISCO PACKET TRACER
6

## Slide 7
Scenarios & Evaluation Metrics
06 • TESTING
Scenario | Test / Command | Observed status | Evidence / metric
Gateway reachability | HR-PC1 → 192.168.10.1 | Pass | 4/4 replies in captured test
Inter-VLAN routing | HR-PC1 → 192.168.20.21 | Pass | 4/4 replies in captured test
Server reachability | HR-PC1 → 192.168.10.10 | Pass | 4/4 replies in captured test
DNS resolution | ping company.local | Pass | Resolved to 192.168.10.10
Sales → HR restriction | Sales-PC1 → 192.168.10.21 | Blocked | ACL deny counter increased
Sales → Server | Sales-PC1 → 192.168.10.10 | Pass | 4/4 replies in captured test
DHCP allocation | R1 show ip dhcp binding | Pass | 9 client leases shown
Port security | SW1 show port-security | Configured | Fa0/1–Fa0/9; max 1 MAC
Use only the captured tests as results; do not claim tests that have not been run.
SMALL OFFICE NETWORK | CISCO PACKET TRACER
7

## Slide 8
Results: Baseline vs Proposed
07 • RESULTS
Baseline (conceptual flat network)
Proposed segmented network
BASELINE CHARACTERISTICS
• One broad broadcast domain • Department traffic not logically separated • Manual addressing may be needed • No demonstrated department ACL boundary
IMPLEMENTED CHARACTERISTICS
• Three department VLANs • DHCP bindings for 9 PCs • Routing through three subinterfaces • ACL blocks Sales-to-HR subnet traffic • DNS + HTTP server access verified
No numerical baseline measurements were collected; comparison is feature-based, not a measured performance claim.
SMALL OFFICE NETWORK | CISCO PACKET TRACER
8
Notes: “Now, I will explain the results of our project.
In a traditional flat network, all departments share a broad broadcast domain. This provides less logical separation between departments.
In our proposed network, we implemented three VLANs: VLAN 10 for HR, VLAN 20 for IT, and VLAN 30 for Sales.
We successfully verified DHCP allocation for nine PCs, inter-VLAN routing, and access to our internal DNS and HTTP server.
We also configured an ACL that blocks traffic from the Sales subnet to the HR subnet while allowing Sales to access the company server.
Therefore, our proposed network provides better segmentation, automated IP addressing, and controlled access compared with the conceptual flat-network baseline.”

## Slide 9
Analysis, Limitations & Security Considerations
08 • ANALYSIS
WHAT WORKS
• VLANs and trunk are active • DHCP issued 9 client addresses • DNS and server reachability verified • ACL counters show matching traffic
LIMITATIONS
• One router and one switch: single points of failure • No Internet/WAN connection in current scope • No measured throughput or delay baseline • DNS/HTTP are internal services; HTTPS must be separately configured
SECURITY NOTES
• Port security helps limit unknown MACs per access port • ACL is directional and ordered top-to-bottom • ICMP success/failure alone does not prove all application policies
NEXT IMPROVEMENTS
• SSH for encrypted device management • Centralized Syslog • DHCP Snooping / DAI if supported • Redundant links/devices and backups
SMALL OFFICE NETWORK | CISCO PACKET TRACER
9
Notes: “Next, I will discuss our project's analysis, limitations, and security considerations.
First, the main features are working as expected. Our VLANs and trunk are active, DHCP has assigned addresses to nine PCs, and DNS and server connectivity have been verified.
We also checked the ACL rules and their match counters to verify traffic filtering.
However, our current design has some limitations. We use only one router and one switch, so they are single points of failure. The project does not include an Internet connection, and we have not measured network throughput or delay.
From a security perspective, port security helps restrict the MAC addresses allowed on access ports. The ACL processes rules in order and is applied in a specific direction.
As future improvements, we can implement SSH for encrypted device management, centralized Syslog monitoring, additional Layer 2 security features where supported, and redundant devices and links.”

## Slide 10
Conclusion, Future Work & References
09 • CLOSING
Conclusion
• Built a segmented office LAN with HR, IT and Sales VLANs.
• Automated client addressing through router-based DHCP.
• Enabled inter-VLAN routing and internal DNS/HTTP services.
• Applied ACL and port security controls and verified key scenarios.
Future work
• SSH administration and stronger management-plane access.
• Centralized Syslog and monitoring.
• Additional Layer 2 protections, if device support allows.
• Redundancy, configuration backups and measured performance tests.
References
• Cisco Networking Academy — Packet Tracer learning resources (https://www.netacad.com/)
• Cisco IOS configuration guides — VLANs, DHCP, ACLs, SSH and port security (https://www.cisco.com/)
• RFC 1918 — Address Allocation for Private Internets (https://www.rfc-editor.org/rfc/rfc1918)
SMALL OFFICE NETWORK | CISCO PACKET TRACER
10
Notes: “To conclude, we successfully designed and implemented a segmented small office network using Cisco Packet Tracer.
We separated HR, IT, and Sales using VLANs, automated IP address allocation through DHCP, and enabled inter-VLAN routing.
We also configured an internal DNS and HTTP server and implemented ACL and port-security controls.
Our testing verified the main network functions and the intended Sales-to-HR access restriction.
In the future, we plan to enhance the network with SSH-based secure administration, centralized logging, additional security protections, configuration backups, and network redundancy.
We referred to Cisco Networking Academy resources, Cisco IOS configuration guides, and RFC 1918 for private IPv4 addressing.
Thank you. I am ready to answer any questions.”